***************************Default***************************
RPi4B+ Raspberry Pi O/S
with multiple Picos connected on USB
Programming the Pico with picotool
05/18/2022
***************************Default***************************

The first shell is running the picotool as root

The 2nd shell is running minicom for test-read freeRTOS (klt-feature-detect & dwt lifting) step or
rp2040-logic-analyzer

The 3rd shell is being used to run lsub to find the the address of the pico connected on USB

The 4th shell is running the cat command on /dev/ttyACM1 which is a multico pico sampling the
built in temperature sensor.

Two pico are connected to RPi4B+ 8Gb

/dev/ttyACM0 /dev/ttyACM1

The first pico is programmed with freeRTOS running test-read.elf
Using minicom see the output
The 2nd pico is program showing 2 cores reading the onboard temp sensor.
The output of the 2nd pico is obtained by using the cat /dev/ttyACM1
devel@pi4-27:~ $ lsusb
Bus 002 Device 001: ID 1d6b:0003 Linux Foundation 3.0 root hub
Bus 001 Device 008: ID 2e8a:000a Raspberry Pi Pico
Bus 001 Device 010: ID 2e8a:000a Raspberry Pi Pico
Bus 001 Device 005: ID 046d:c534 Logitech, Inc. Unifying Receiver
Bus 001 Device 003: ID 058f:6254 Alcor Micro Corp. USB Hub
Bus 001 Device 002: ID 2109:3431 VIA Labs, Inc. Hub
Bus 001 Device 001: ID 1d6b:0002 Linux Foundation 2.0 root hub

devel@pi4-27:~ $ sudo su
root@pi4-27:/home/devel# . Ultibo_Projects/picoultibo.sh
/home/devel/ultibo/core:/home/devel/qemu-6.2.0-rpios/bin:/home/devel/local/openocd/bin:/home/devel/picotool/build/:/usr/local/sbin:/usr/local/bin:/usr/sbin:/usr/bin:/sbin:/bin
root@pi4-27:/home/devel# picotool info
No accessible RP2040 devices in BOOTSEL mode were found.

but:

Device at bus 1, address 4 appears to be a RP2040 device with a USB serial
    connection, so consider -f (or -F) to force reboot in order to run the
    command.
Device at bus 1, address 6 appears to be a RP2040 device with a USB serial
    connection, so consider -f (or -F) to force reboot in order to run the
    command.
root@pi4-27:/home/devel# picotool info --bus 1 --address 4
No accessible RP2040 device in BOOTSEL mode was found at bus 1, address 4.

but:

Device at bus 1, address 4 appears to be a RP2040 device with a USB serial
    connection, so consider -f (or -F) to force reboot in order to run the
    command.
root@pi4-27:/home/devel# picotool info --bus 1 --address 4 -f -a
The device was asked to reboot into BOOTSEL mode so the command can be executed.

Program Information
 name: test-read
 features: USB stdin / stdout
 binary start: 0x10000000
 binary end: 0x10016034

Fixed Pin Information
 none

Build Information
 sdk version: 1.3.0
 pico_board: pico
 boot2_name: boot2_w25q080
 build date: May 16 2022
 build attributes: Release

Device Information
 flash size: 2048K
 ROM version: 2

        The device was asked to reboot back into application mode.
root@pi4-27:/home/devel# picotool info --bus 1 --address 6 -f -a
The device was asked to reboot into BOOTSEL mode so the command can be executed.

Program Information
 name: multicore
 features: USB stdin / stdout
 binary start: 0x10000000
 binary end: 0x10007ea8

Fixed Pin Information
 none

Build Information
 sdk version: 1.3.0
 pico_board: pico
 boot2_name: boot2_w25q080
 build date: May 16 2022
 build attributes: Release

Device Information
 flash size: 2048K
 ROM version: 2

devel@pi4-27:~ $ sudo cat /dev/ttyACM1
Temp = 27.138449 C

Temp = 27.606592 C

Temp = 27.138449 C

Temp = 27.138449 C

Temp = 27.138449 C

The pico on /dev/ttyAMC0 can also run the logic-analyzer
root@pi4-27:/home/devel# picotool load /home/devel/rp2040-freertos-project/build/rp2040-logic-analyzer/rp2040-logic-analyzer.elf --bus 1 --address 18 -f
        The device was asked to reboot back into application mode.

lsusb -v

Bus 002 Device 001: ID 1d6b:0003 Linux Foundation 3.0 root hub
Couldn't open device, some information will be missing
Device Descriptor:
  bLength 18
  bDescriptorType 1
  bcdUSB 3.00
  bDeviceClass 9 Hub
  bDeviceSubClass 0
  bDeviceProtocol 3
  bMaxPacketSize0 9
  idVendor 0x1d6b Linux Foundation
  idProduct 0x0003 3.0 root hub
  bcdDevice 5.10
  iManufacturer 3 Linux 5.10.92-v7l+ xhci-hcd
  iProduct 2 xHCI Host Controller
  iSerial 1 0000:01:00.0
  bNumConfigurations 1
  Configuration Descriptor:
    bLength 9
    bDescriptorType 2
    wTotalLength 0x001f
    bNumInterfaces 1
    bConfigurationValue 1
    iConfiguration 0
    bmAttributes 0xe0
      Self Powered
      Remote Wakeup
    MaxPower 0mA
    Interface Descriptor:
      bLength 9
      bDescriptorType 4
      bInterfaceNumber 0
      bAlternateSetting 0
      bNumEndpoints 1
      bInterfaceClass 9 Hub
      bInterfaceSubClass 0
      bInterfaceProtocol 0 Full speed (or root) hub
      iInterface 0
      Endpoint Descriptor:
        bLength 7
        bDescriptorType 5
        bEndpointAddress 0x81 EP 1 IN
        bmAttributes 3
        Transfer Type Interrupt
        Synch Type None
        Usage Type Data
        wMaxPacketSize 0x0004 1x 4 bytes
        bInterval 12
        bMaxBurst 0

Bus 001 Device 030: ID 2e8a:000a Raspberry Pi Pico
Couldn't open device, some information will be missing
Device Descriptor:
  bLength 18
  bDescriptorType 1
  bcdUSB 2.00
  bDeviceClass 239 Miscellaneous Device
  bDeviceSubClass 2
  bDeviceProtocol 1 Interface Association
  bMaxPacketSize0 64
  idVendor 0x2e8a
  idProduct 0x000a
  bcdDevice 1.00
  iManufacturer 1 Raspberry Pi
  iProduct 2 Pico
  iSerial 3 E66034F71F1F4F36
  bNumConfigurations 1
  Configuration Descriptor:
    bLength 9
    bDescriptorType 2
    wTotalLength 0x0054
    bNumInterfaces 3
    bConfigurationValue 1
    iConfiguration 0
    bmAttributes 0x80
      (Bus Powered)
    MaxPower 250mA
    Interface Association:
      bLength 8
      bDescriptorType 11
      bFirstInterface 0
      bInterfaceCount 2
      bFunctionClass 2 Communications
      bFunctionSubClass 2 Abstract (modem)
      bFunctionProtocol 0
      iFunction 0
    Interface Descriptor:
      bLength 9
      bDescriptorType 4
      bInterfaceNumber 0
      bAlternateSetting 0
      bNumEndpoints 1
      bInterfaceClass 2 Communications
      bInterfaceSubClass 2 Abstract (modem)
      bInterfaceProtocol 0
      iInterface 4
      CDC Header:
        bcdCDC 1.20
      CDC Call Management:
        bmCapabilities 0x00
        bDataInterface 1
      CDC ACM:
        bmCapabilities 0x02
        line coding and serial state
      CDC Union:
        bMasterInterface 0
        bSlaveInterface 1
      Endpoint Descriptor:
        bLength 7
        bDescriptorType 5
        bEndpointAddress 0x81 EP 1 IN
        bmAttributes 3
        Transfer Type Interrupt
        Synch Type None
        Usage Type Data
        wMaxPacketSize 0x0008 1x 8 bytes
        bInterval 16
    Interface Descriptor:
      bLength 9
      bDescriptorType 4
      bInterfaceNumber 1
      bAlternateSetting 0
      bNumEndpoints 2
      bInterfaceClass 10 CDC Data
      bInterfaceSubClass 0
      bInterfaceProtocol 0
      iInterface 0
      Endpoint Descriptor:
        bLength 7
        bDescriptorType 5
        bEndpointAddress 0x02 EP 2 OUT
        bmAttributes 2
        Transfer Type Bulk
        Synch Type None
        Usage Type Data
        wMaxPacketSize 0x0040 1x 64 bytes
        bInterval 0
      Endpoint Descriptor:
        bLength 7
        bDescriptorType 5
        bEndpointAddress 0x82 EP 2 IN
        bmAttributes 2
        Transfer Type Bulk
        Synch Type None
        Usage Type Data
        wMaxPacketSize 0x0040 1x 64 bytes
        bInterval 0
    Interface Descriptor:
      bLength 9
      bDescriptorType 4
      bInterfaceNumber 2
      bAlternateSetting 0
      bNumEndpoints 0
      bInterfaceClass 255 Vendor Specific Class
      bInterfaceSubClass 0
      bInterfaceProtocol 1
      iInterface 5

Bus 001 Device 010: ID 2e8a:000a Raspberry Pi Pico
Couldn't open device, some information will be missing
Device Descriptor:
  bLength 18
  bDescriptorType 1
  bcdUSB 2.00
  bDeviceClass 239 Miscellaneous Device
  bDeviceSubClass 2
  bDeviceProtocol 1 Interface Association
  bMaxPacketSize0 64
  idVendor 0x2e8a
  idProduct 0x000a
  bcdDevice 1.00
  iManufacturer 1 Raspberry Pi
  iProduct 2 Pico
  iSerial 3 E6605838838BA92F
  bNumConfigurations 1
  Configuration Descriptor:
    bLength 9
    bDescriptorType 2
    wTotalLength 0x0054
    bNumInterfaces 3
    bConfigurationValue 1
    iConfiguration 0
    bmAttributes 0x80
      (Bus Powered)
    MaxPower 250mA
    Interface Association:
      bLength 8
      bDescriptorType 11
      bFirstInterface 0
      bInterfaceCount 2
      bFunctionClass 2 Communications
      bFunctionSubClass 2 Abstract (modem)
      bFunctionProtocol 0
      iFunction 0
    Interface Descriptor:
      bLength 9
      bDescriptorType 4
      bInterfaceNumber 0
      bAlternateSetting 0
      bNumEndpoints 1
      bInterfaceClass 2 Communications
      bInterfaceSubClass 2 Abstract (modem)
      bInterfaceProtocol 0
      iInterface 4
      CDC Header:
        bcdCDC 1.20
      CDC Call Management:
        bmCapabilities 0x00
        bDataInterface 1
      CDC ACM:
        bmCapabilities 0x02
        line coding and serial state
      CDC Union:
        bMasterInterface 0
        bSlaveInterface 1
      Endpoint Descriptor:
        bLength 7
        bDescriptorType 5
        bEndpointAddress 0x81 EP 1 IN
        bmAttributes 3
        Transfer Type Interrupt
        Synch Type None
        Usage Type Data
        wMaxPacketSize 0x0008 1x 8 bytes
        bInterval 16
    Interface Descriptor:
      bLength 9
      bDescriptorType 4
      bInterfaceNumber 1
      bAlternateSetting 0
      bNumEndpoints 2
      bInterfaceClass 10 CDC Data
      bInterfaceSubClass 0
      bInterfaceProtocol 0
      iInterface 0
      Endpoint Descriptor:
        bLength 7
        bDescriptorType 5
        bEndpointAddress 0x02 EP 2 OUT
        bmAttributes 2
        Transfer Type Bulk
        Synch Type None
        Usage Type Data
        wMaxPacketSize 0x0040 1x 64 bytes
        bInterval 0
      Endpoint Descriptor:
        bLength 7
        bDescriptorType 5
        bEndpointAddress 0x82 EP 2 IN
        bmAttributes 2
        Transfer Type Bulk
        Synch Type None
        Usage Type Data
        wMaxPacketSize 0x0040 1x 64 bytes
        bInterval 0
    Interface Descriptor:
      bLength 9
      bDescriptorType 4
      bInterfaceNumber 2
      bAlternateSetting 0
      bNumEndpoints 0
      bInterfaceClass 255 Vendor Specific Class
      bInterfaceSubClass 0
      bInterfaceProtocol 1
      iInterface 5

Bus 001 Device 005: ID 046d:c534 Logitech, Inc. Unifying Receiver
Couldn't open device, some information will be missing
Device Descriptor:
  bLength 18
  bDescriptorType 1
  bcdUSB 2.00
  bDeviceClass 0
  bDeviceSubClass 0
  bDeviceProtocol 0
  bMaxPacketSize0 8
  idVendor 0x046d Logitech, Inc.
  idProduct 0xc534 Unifying Receiver
  bcdDevice 29.01
  iManufacturer 1 Logitech
  iProduct 2 USB Receiver
  iSerial 0
  bNumConfigurations 1
  Configuration Descriptor:
    bLength 9
    bDescriptorType 2
    wTotalLength 0x003b
    bNumInterfaces 2
    bConfigurationValue 1
    iConfiguration 4
    bmAttributes 0xa0
      (Bus Powered)
      Remote Wakeup
    MaxPower 98mA
    Interface Descriptor:
      bLength 9
      bDescriptorType 4
      bInterfaceNumber 0
      bAlternateSetting 0
      bNumEndpoints 1
      bInterfaceClass 3 Human Interface Device
      bInterfaceSubClass 1 Boot Interface Subclass
      bInterfaceProtocol 1 Keyboard
      iInterface 0
        HID Device Descriptor:
        bLength 9
        bDescriptorType 33
        bcdHID 1.11
        bCountryCode 0 Not supported
        bNumDescriptors 1
        bDescriptorType 34 Report
        wDescriptorLength 59
        Report Descriptors:
        ** UNAVAILABLE **
      Endpoint Descriptor:
        bLength 7
        bDescriptorType 5
        bEndpointAddress 0x81 EP 1 IN
        bmAttributes 3
        Transfer Type Interrupt
        Synch Type None
        Usage Type Data
        wMaxPacketSize 0x0008 1x 8 bytes
        bInterval 8
    Interface Descriptor:
      bLength 9
      bDescriptorType 4
      bInterfaceNumber 1
      bAlternateSetting 0
      bNumEndpoints 1
      bInterfaceClass 3 Human Interface Device
      bInterfaceSubClass 1 Boot Interface Subclass
      bInterfaceProtocol 2 Mouse
      iInterface 0
        HID Device Descriptor:
        bLength 9
        bDescriptorType 33
        bcdHID 1.11
        bCountryCode 0 Not supported
        bNumDescriptors 1
        bDescriptorType 34 Report
        wDescriptorLength 177
        Report Descriptors:
        ** UNAVAILABLE **
      Endpoint Descriptor:
        bLength 7
        bDescriptorType 5
        bEndpointAddress 0x82 EP 2 IN
        bmAttributes 3
        Transfer Type Interrupt
        Synch Type None
        Usage Type Data
        wMaxPacketSize 0x0014 1x 20 bytes
        bInterval 2

Bus 001 Device 003: ID 058f:6254 Alcor Micro Corp. USB Hub
Couldn't open device, some information will be missing
Device Descriptor:
  bLength 18
  bDescriptorType 1
  bcdUSB 2.00
  bDeviceClass 9 Hub
  bDeviceSubClass 0
  bDeviceProtocol 1 Single TT
  bMaxPacketSize0 64
  idVendor 0x058f Alcor Micro Corp.
  idProduct 0x6254 USB Hub
  bcdDevice 1.00
  iManufacturer 0
  iProduct 1 USB2.0Hub
  iSerial 0
  bNumConfigurations 1
  Configuration Descriptor:
    bLength 9
    bDescriptorType 2
    wTotalLength 0x0019
    bNumInterfaces 1
    bConfigurationValue 1
    iConfiguration 0
    bmAttributes 0xe0
      Self Powered
      Remote Wakeup
    MaxPower 100mA
    Interface Descriptor:
      bLength 9
      bDescriptorType 4
      bInterfaceNumber 0
      bAlternateSetting 0
      bNumEndpoints 1
      bInterfaceClass 9 Hub
      bInterfaceSubClass 0
      bInterfaceProtocol 0 Full speed (or root) hub
      iInterface 0
      Endpoint Descriptor:
        bLength 7
        bDescriptorType 5
        bEndpointAddress 0x81 EP 1 IN
        bmAttributes 3
        Transfer Type Interrupt
        Synch Type None
        Usage Type Data
        wMaxPacketSize 0x0001 1x 1 bytes
        bInterval 12

Bus 001 Device 002: ID 2109:3431 VIA Labs, Inc. Hub
Couldn't open device, some information will be missing
Device Descriptor:
  bLength 18
  bDescriptorType 1
  bcdUSB 2.10
  bDeviceClass 9 Hub
  bDeviceSubClass 0
  bDeviceProtocol 1 Single TT
  bMaxPacketSize0 64
  idVendor 0x2109 VIA Labs, Inc.
  idProduct 0x3431 Hub
  bcdDevice 4.21
  iManufacturer 0
  iProduct 1 USB2.0 Hub
  iSerial 0
  bNumConfigurations 1
  Configuration Descriptor:
    bLength 9
    bDescriptorType 2
    wTotalLength 0x0019
    bNumInterfaces 1
    bConfigurationValue 1
    iConfiguration 0
    bmAttributes 0xe0
      Self Powered
      Remote Wakeup
    MaxPower 100mA
    Interface Descriptor:
      bLength 9
      bDescriptorType 4
      bInterfaceNumber 0
      bAlternateSetting 0
      bNumEndpoints 1
      bInterfaceClass 9 Hub
      bInterfaceSubClass 0
      bInterfaceProtocol 0 Full speed (or root) hub
      iInterface 0
      Endpoint Descriptor:
        bLength 7
        bDescriptorType 5
        bEndpointAddress 0x81 EP 1 IN
        bmAttributes 3
        Transfer Type Interrupt
        Synch Type None
        Usage Type Data
        wMaxPacketSize 0x0001 1x 1 bytes
        bInterval 12

Bus 001 Device 001: ID 1d6b:0002 Linux Foundation 2.0 root hub
Couldn't open device, some information will be missing
Device Descriptor:
  bLength 18
  bDescriptorType 1
  bcdUSB 2.00
  bDeviceClass 9 Hub
  bDeviceSubClass 0
  bDeviceProtocol 1 Single TT
  bMaxPacketSize0 64
  idVendor 0x1d6b Linux Foundation
  idProduct 0x0002 2.0 root hub
  bcdDevice 5.10
  iManufacturer 3 Linux 5.10.92-v7l+ xhci-hcd
  iProduct 2 xHCI Host Controller
  iSerial 1 0000:01:00.0
  bNumConfigurations 1
  Configuration Descriptor:
    bLength 9
    bDescriptorType 2
    wTotalLength 0x0019
    bNumInterfaces 1
    bConfigurationValue 1
    iConfiguration 0
    bmAttributes 0xe0
      Self Powered
      Remote Wakeup
    MaxPower 0mA
    Interface Descriptor:
      bLength 9
      bDescriptorType 4
      bInterfaceNumber 0
      bAlternateSetting 0
      bNumEndpoints 1
      bInterfaceClass 9 Hub
      bInterfaceSubClass 0
      bInterfaceProtocol 0 Full speed (or root) hub
      iInterface 0
      Endpoint Descriptor:
        bLength 7
        bDescriptorType 5
        bEndpointAddress 0x81 EP 1 IN
        bmAttributes 3
        Transfer Type Interrupt
        Synch Type None
        Usage Type Data
        wMaxPacketSize 0x0004 1x 4 bytes
        bInterval 12